## Slide 1: Battery Current states
Mode | Foreground display, status dot | Notes | Chart msg, status dot
Normal | [T, I, Temp,V, Ah, B%] | Regular monitoring mode | None
Normal, 25%<Batt <75% | [T, I, Temp,V, Ah, B%] | Regular mon. armed for battery condition evaluation | None,
Normal, Batt: 25%-75% | [T, I, Temp,V, Ah, B%] flash | Regular mon. with battery condition evaluation | None, flash
CAL (1) chg to 100% | [CAL: T, I, Temp,V, Ah, B%] | Cal initiated, waiting for 100% charge | Cal: charge to 100%,
CAL (2) 5 min @100% | [CAL-8: T, I, Temp,V, Ah, B%] | Cal in 5 min float charge @ 100% | Cal: float @ 100%,
CAL (3) disconnect charger | [CAL(flash): T, I, Temp,V, Ah, B%] | Waiting for user to disconnect charger | Cal: wait for charger disconnect,
CAL (4) discharge to 99% | [CAL+2: T, I, Temp,V, Ah, B%] flash | Cal waiting for 99% battery state | Cal: discharge to 95%, flash
CAL (5) start msr at 99% | [CAL: T, I, Temp,V, Ah, B%] flash | Cal in measurement mode | Cal: measuring, flash
CAL (6) end msr at 10% | [T, I, Temp,V, Ah, B%] | Cal measurement ends, record data and popup results (Capacity=DmAh/0.89) | None,